## Slide 1
Welcome to
CSA2002 INTRODUCTION TO DRONES
G.GANESAN, B.E (CSE)., M.E (CSE)., M.S(IT).,MISTE.,
SENIOR TEACHING FELLOW,
SCHOOL OF CSE.
+91-9500234437
ganesan.g@vitbhopal.ac.in

## Slide 2: Course Content
Date: 24-01-2023 Time: 10.05am – 11.35am
Connectors
Frames

## Slide 3: Connectors
Connectors are interfaces for routing power, data, and signals to and from different subsystems within the platform.
Route between UAV power and control systems, guidance systems, GNSS/INS and integrated or external payloads such as laser scanners, LiDAR and thermal or visual cameras.
Choosing a connector for a particular UAV application, depends on the design requirements.

## Slide 4: Connectors - Requirements
Size, Weight and Power (SWaP): Lightweight and Compact (small form)
- Payload, fuel, fly for longer.
- Small UAVs
2. Environment and Durability: Variety and harsh environment conditions.
- High vibration and shock environments.
Rough landing and heavy vibration – High sock and vibration tolerance
Weather conditions – Airborne particles – sand, ash, dust, rain, temp
– sealing and protection ratings.
Operating range: -55 to +200 degrees Centigrade.
Electromagnetic Interference and Pulses (EMI and EMP): Shielding
necessary.

## Slide 5: Connectors - Requirements
3. Performance: Signal degradation is the issue in high-speed applications.
- Connectors are capable of transferring large amount of
high-resolution video at ever-increasing speeds.
- Highly insulating materials, allow airflow to protect from melting.

## Slide 6: Connector - Types
Medium or High altitude Connectors
Custom and COTS (commercial off-the-shelf) connectors are in a variety of form factors, such as Circular, Rectangular/ Strip.
Technology standard form factors such as USB, Ethernet and D-sub.
OEMs (Original Equipment Manufacturers) – MIL-SPEC or MIL-STD – which are meet the specification factors such as Vibration, Durability, Corrosion, and Temperature.

## Slide 7: Connector - Types
Coupling and Locking Methods:
Plastic or metal shells.
Metalized composite shells providing lightweight and durable and reduce overall weight.
Aluminum-Higher-end to provide EMC protection.
Ruggedized Push-Pull:
Shell material used for connector bodies.
Provides both protection and Strength, but add weight.
Fischer:
Rugged and mission-critical applications.
Available: push-pull, screw lock, and quick release.

## Slide 8: Connector - Types
TE Connectivity:
Lightweight, rugged interconnect tech.
For Unmanned vehicles like: UAV, UGV, UUV.
High performance – To absorb high levels of
vibration, shock and impact.
Nicomatic:
Power and Video transmission.
MIL 83513 performance –> 1.27mm pitch of rugged Micro connectors.

## Slide 9
QUERIES?

## Slide 10: FRAMES

## Slide 11: Frames
Drone’s body skeleton is called frame. It helps to mount the motors, battery, and their parts on it. The frame is used to built copter or glider.
Ex: Tricopter – size is small, 3-motors, 3-propellers, 3-ESC, etc.
Material: Carbon, Wood, Metal, Plastic, Fiberglass.
Choosing: Light and Strong – Carbon Fiber (high cost)
- Plastic / Acrylic (medium cost)
We keep the frame balanced and the center of gravity when flying the drone.

## Slide 12: Frames – How to built?
The thrust of the motor after mounting on the frame is really important.
Thrust tells – float in the air or fall down or become imbalanced.
Thrust of a Motor:
If ‘P’ is the payload capacity of the drone, then the motor thrust ‘T’ is:
Where, M – No.of Motors, W – Weight of the drone, H-Hover throttle in %.
Therefore, P = T x M x H - W

## Slide 13: Frames - Types
Monocopter
Bicopter
Tricopter: T Y
Quadcopter: + X H
Hexacopter: X Stretch
Octocopter: + X

## Slide 14: Frames – Pros and Cons
1. Monocopter: Up and Down only. Increase the motor helps to stabilize the
drone. Yaw, Rudder, and Roll motions are not possible.
2. Bicopter: Varying speed of motor independently to generate total thrust.
3. Tricopter: Different look for a UAV. Forward motion. Low cost.
Not symmetric ->Servo needs to be mounted along the axis that
leads rear arm is more complex, therefore not all FC support this
configuration.
4. Quadcopter: Simplest construction and quite versatile. The arms/motor are
symmetric about two axes. All FC can work.
No redundancy. If there is a failure in system (motor/propeller), the
craft going to crash.

## Slide 15: Frames – Pros and Cons
5. Hexacopter: Add 2 more arms and motors -> Lift more payload.
If a motor fail, a chance to land rather than crash.
Moduler -> use the same motor and support arm.
All FC can support.
More expensive and larger.
Adding motor/arms -> increase the copter weight -> battery
6. Octocopter: Increased redundancy -> more motors = more thrust
More motors = more price and larger battery pack.

## Slide 16: Frames – Guidelines
Step 1: See what materials and machining processes you have at your disposal.
If you do not have much as far as machining capabilities, are not comfortable with tools, or simply want a more professional frame, then consider purchasing a frame kit.
A decent frame can be made with basic tools and materials, but determining areas where it may be structurally weak, resonate (cause vibration) or may be misaligned take a keen eye and experience
If you plan to create a custom frame, take into consideration all of the
mounting which needs to be done; motors, electronics etc. and plan accordingly.

## Slide 17: Frames – Guidelines
Step 2: List all of the additional (non-essential) parts you plan to add
Additional items might include: one, two or three axis camera gimbal, parachute, onboard mini computer, payload, long-range electronics (tend to be larger / heavier), floatation etc.
This list of additional / non-essential parts will give you an idea of the size of drone you will need, and add to the total weight calculation (to be done later).
Step 3: Get a rough idea of the size of frame you want
A larger frame does not necessarily make the drone more capable, and a smaller frame does not mean the drone will be any less expensive
A drone between 400 and 600mm is suggested for beginners.

## Slide 18: Frames – Guidelines
Step 4: Design, build and test the frame
If you opted to purchase a frame kit, you should not have much to worry about in regards to durability / rigidity / assembly.
If you chose instead to design and build your own frame, it's important to test its durability, check the weight and see if it can withstand vibration.
Consider using a CAD software (many are free such as Google Sketchup) to design the frame and ensure dimensions are correct.

## Slide 19
Thank You
&
Queries?