## Slide 1
Welcome to
CSA2002 INTRODUCTION TO DRONES
G.GANESAN, B.E (CSE)., M.E (CSE)., M.S(IT).,MISTE.,
SENIOR TEACHING FELLOW,
SCHOOL OF CSE.
+91-9500234437
ganesan.g@vitbhopal.ac.in

## Slide 2: Course Content
Date: 25-01-2023 Time: 10.05am – 11.35am
Assembling the Drone
Aerodynamics to fly a Drone

## Slide 3: Assembling the Drone
For a small drone with stable flight performance
3D mechanical frame
STEVAL-FCU001V1 board
1-cell battery 3.V 600mAh 30C
2xCW, 2xCCW coreless DC motor
8.5x20mm
4x65mm propellers
Remote Controller or Smartphone App.

## Slide 4: Motor Placing
To support the air flow for CW and CCW motors, the three arms to sustain the
motors have been designed as airfoils.
Take a look to
orientation of airfoils
CW
CCW
Front Direction
CCW
CW

## Slide 5: Assembling the Drone
Assembling the Frame (HobbyKing-S500)
Frame arms – 4
Leg Plates – 4
Rod for the base mount – 2
Top plate – 1
Bottom plate – 1
(mounting the power lines)
Screws – requirable

## Slide 6: Mounting - Motors
Place the motor on the frame arm and attach by the screws.
BLDC has three wires coming out of the motor.
Solder the bullet connector to them to be connected to the ESC.
Connect other three motors to the frame arms.

## Slide 7: Mounting - Motors
Each motor needed 3 wires  3 x 4 = 12 wires
Single ESC has 8 wires – 3 for motor, 2 for power unit, 3 for signal, ground,
and power.

## Slide 8: Mounting - Motors
Suppose we configure the ESC with Arduino
The main wire is used as signal instead the Power of the ESC cable.

## Slide 9: Connecting ArduPilot
ArduPilot task is for flying and controlling the drone, basically brain of the drone.
It enables the drone to control the movement, the camera, and the other sensors connected to it.
If we connect radio to ArduPilot, then we can control the drone remotely.
The three wires of the ESCs are connected with the ArduPilot. We can add up to 8 ESCs.

## Slide 10: Connecting ArduPilot

## Slide 11: Connecting ArduPilot
Connect the signal, Power, and ground pins of ESC with the ArduPilot.

## Slide 12: Connecting with Common Power Module
Two types – Normal and Pusher
Normal – rotates anticlockwise
Pusher – rotates clockwise and it denoted by P or R.
The common power module provides 5.37V and 2.25 Amp power supply.
It allows the ArduPilot to work more accurately with a lot of sensors connected to it, such as the compass sensor.
A small variation of the power will cause the direction to go wrong. Using a common power module to these pins is needed for getting good accuracy of the measurements from the sensors connected to and built into the ArduPilot.

## Slide 13: Connecting with Common Power Module
A Bluetooth device or an RF transceiver (having 900 MHz or 2.4 GHz ) is connected for communicate with GCS.
The range of cover up is 50m or the radius, which depends upon the device.
Wirelessly we can connect our drone to the computer and download flight data.
Radio’s are short-range or long-range types.
3DR radio is easy to set up via the ArduPilot software and easy to use.
The radio directly connected to the ArduPilot and it send signals to the receiver connected to the computer.
The radio will connected via the “Telem port”.

## Slide 14: Connecting RC Receiver
Pin configuration in ArduPilot
Pin-1: Roll / aileron
Pin-2: Pitch / elevator
Pin-3: Throttle
Pin-4: Yaw / Rudder
Pin-5: Auxiliary channel-1 (Ex: mode switch)
Pin-6: Auxiliary channel-2

## Slide 15: Connecting Battery
Frame is S500, it come with a board.
Connect the battery by soldering the connectors to the board and later just plug the battery while flying the drone.
Use Zipties to lock the battery under the body of the copter.

## Slide 16: Connection Summary
The BLDC motors connected to the four-in-one ESC.
The ESC connected to the ArduPilot’s output pins (signal cables, 5V, ground)
The power cables of the ESC directly connected to the battery.
The Radio and the RC receiver connected to the Telem pins and input pins of the ArduPilot respectively.

## Slide 17: Connection Testing
Connect the battery to the ESC. The ESC will make a beeping sound and the RC receiver show an LED blinking.
Turn on the RC transmitter after installing the battery to it.
Press and hold the Bind Range Test button until LED of the RC receiver stop blinking. Do this if the LED does not stop blinking or try switch off or disconnect the binding cable from the RC receiver.

## Slide 18: Connection Testing
Rising or Climbing or Taking off
To fly the drone over the ground, we need force against gravitation.
The motion of the object based on Newton’s second law from the weight of the drone W = mg.
force = mass x acceleration (linear)
The torque can be defined with the help of inertia:
Torque = Inertia x acceleration (angular)

## Slide 19: Connection Testing
Now, we change the equation as
mg < F1 + F2 + F3 + F4 (Quadcopter)
D* = F1+F2+F3+F4 – mg >0
When considering Yaw motion – there is difference movements between any pair of propellers. If there is a stable upward force and the propeller forces, then
Izz = M1+M2+M3+M4

## Slide 20: Connection Testing
Saving from Crashing
Field - Open space without trees and electrical wires.
Lift – No sudden lift – High throttle but gradually and stabilize
Yaw – Start the yawing in parallel to the surface.
Pitch – Move the drone in a forward or backward direction.
Roll – Rotate the roll gently without any nervous.
Note: Do not press any button of the transmitter without knowing its tasks.
* Check the weather, obstacles, and air flow.

## Slide 21: Connection Testing
Security Protocols
Cannot fly within 5 miles of an airport.
Keep within your eyesight.
Keep the height limit is 400 feet (0.12 km)
Cannot fly in busy traffic areas.
Register and get license for business or professional.
Must know the local area rules.

## Slide 22
QUERIES?

## Slide 23: AERODYNAMICS

## Slide 24: Introduction
Aerodynamic is the study of forces and the resulting motion of objects through the air.
Studying the motion of air around an object allows us to measure the forces of lift, which allows an aircraft to overcome gravity, and drag, which is the resistance an aircraft “feels” as it moves through the air. Everything moving through the air (including airplanes, rockets, and birds) is affected by aerodynamics.

## Slide 25: Introduction
1. Air in Motion:
As an airplane moves through the air, its wings cause changes in the speed and pressure of the air moving past them. These changes result in the upward force called lift.
Air Pressure: Normal, Low, and Very Low.
Why does the air speed up?
If the area in which the air is moving narrow or widens, then the air has to speed up or slow down to maintain a constant amount of air moving through the area.

## Slide 26: Introduction
2. Friction Drag:
Friction is the resistance that happens when two things rub together.
When an object moves through air, the air closest to the object’s surface is dragged along with it, pulling or rubbing at the air that it passes. This rubbing exerts a force on the object opposite to the direction of motion—friction drag.
The thin layer of air closest to the surface of a moving object is called the boundary layer. This is where friction drag occurs.

## Slide 27: Introduction
3. Vortex Drag:
The spirals of air that trail off the tips of an airplane’s wings also contribute to drag. These wing tip vortices steal energy from the motion of the airplane, creating vortex drag.
The higher-pressure air below a wing spills up over the wing tip into the area of lower-pressure air above. The wing’s forward motion spins this upward spill of air into a long spiral, like a small tornado, that trails off the wing tip. These wing tip vortices create a form of pressure drag called vortex drag.

## Slide 28: Introduction
4. Shock Wave:
When airplane travels less than the speed of sound, the pressure waves created by the airplane being smooth and gradual.
When an airplane reaches the speed of sound and catches up to its own pressure waves, the air ahead of it receives no warning of the plane’s approach. The airplane plows through the air, creating a shock wave.
As air flows through the shock wave, its pressure, density, and temperature all increases.

## Slide 29: Frames – How to built?
The thrust of the motor after mounting on the frame is really important.
Thrust tells – float in the air or fall down or become imbalanced.
Thrust of a Motor:
If ‘P’ is the payload capacity of the drone, then the motor thrust ‘T’ is:
Where, M – No.of Motors, W – Weight of the drone, H-Hover throttle in %.
Therefore, P = T x M x H - W

## Slide 30: Frames - Types
Monocopter
Bicopter
Tricopter: T Y
Quadcopter: + X H
Hexacopter: X Stretch
Octocopter: + X

## Slide 31: Frames – Pros and Cons
1. Monocopter: Up and Down only. Increase the motor helps to stabilize the
drone. Yaw, Rudder, and Roll motions are not possible.
2. Bicopter: Varying speed of motor independently to generate total thrust.
3. Tricopter: Different look for a UAV. Forward motion. Low cost.
Not symmetric ->Servo needs to be mounted along the axis that
leads rear arm is more complex, therefore not all FC support this
configuration.
4. Quadcopter: Simplest construction and quite versatile. The arms/motor are
symmetric about two axes. All FC can work.
No redundancy. If there is a failure in system (motor/propeller), the
craft going to crash.

## Slide 32: Frames – Pros and Cons
5. Hexacopter: Add 2 more arms and motors -> Lift more payload.
If a motor fail, a chance to land rather than crash.
Moduler -> use the same motor and support arm.
All FC can support.
More expensive and larger.
Adding motor/arms -> increase the copter weight -> battery
6. Octocopter: Increased redundancy -> more motors = more thrust
More motors = more price and larger battery pack.

## Slide 33: Frames – Guidelines
Step 1: See what materials and machining processes you have at your disposal.
If you do not have much as far as machining capabilities, are not comfortable with tools, or simply want a more professional frame, then consider purchasing a frame kit.
A decent frame can be made with basic tools and materials, but determining areas where it may be structurally weak, resonate (cause vibration) or may be misaligned take a keen eye and experience
If you plan to create a custom frame, take into consideration all of the
mounting which needs to be done; motors, electronics etc. and plan accordingly.

## Slide 34: Frames – Guidelines
Step 2: List all of the additional (non-essential) parts you plan to add
Additional items might include: one, two or three axis camera gimbal, parachute, onboard mini computer, payload, long-range electronics (tend to be larger / heavier), floatation etc.
This list of additional / non-essential parts will give you an idea of the size of drone you will need, and add to the total weight calculation (to be done later).
Step 3: Get a rough idea of the size of frame you want
A larger frame does not necessarily make the drone more capable, and a smaller frame does not mean the drone will be any less expensive
A drone between 400 and 600mm is suggested for beginners.

## Slide 35: Frames – Guidelines
Step 4: Design, build and test the frame
If you opted to purchase a frame kit, you should not have much to worry about in regards to durability / rigidity / assembly.
If you chose instead to design and build your own frame, it's important to test its durability, check the weight and see if it can withstand vibration.
Consider using a CAD software (many are free such as Google Sketchup) to design the frame and ensure dimensions are correct.

## Slide 36
Thank You
&
Queries?