## Slide 1
Welcome to
CSA2002 INTRODUCTION TO DRONES
G.GANESAN, B.E (CSE)., M.E (CSE)., M.S(IT).,MISTE.,
SENIOR TEACHING FELLOW,
SCHOOL OF CSE.
+91-9500234437
ganesan.g@vitbhopal.ac.in

## Slide 2: Course Content
Date: 30, 31-01-2023 Time: 10.05am – 11.35am
1. How to built a Drones.
- Preparing
- ARM Planner
2. Building Follow me Drone
3. Building Arduino Based Drone

## Slide 3: Preparing
Goal: Learn about using the ESP8266 module with
ArduPilot and Arduino.
Requirements:
ESP8266 module
Arduino board
ArduPilot software
Smartphone
Connecting wires
Program

## Slide 4: Preparing
1. Connect the ESP8266 to Arduino
The pin configurations are:
This configuration used to control
LED with the ESP8266.
ESP8266 | Arduino
RX | 3
TX | 2
VCC | 3V
CH_PD | 3V
GPIO 0 | No connection
GPIO 1 | No connection

## Slide 5: Preparing
2. Installing Libraries and Mobile App
In Linux  usr/share/Arduino/Libraries - Update the library.
Connect the ESP8266 to the Arduino.
Download “Blynk” Mobile application fro App Store / Play Store.
Install the application and finish the registration process, if required.

## Slide 6: Preparing
LED Project
Choose Device: Arduino UNO
Connection Type: WiFi
Theme: DARK / LIGHT
Create Project

## Slide 7: Preparing
3. Get Authentication
When create a project, we will get prompt that an authentication code, that sent to our mail.
The authentication code also present in the project setting of the Blynk application.
Swipe right ride of your screen to access the Widget menu and select a Button from there:

## Slide 8: Preparing

## Slide 9: Preparing
4. Write the Arduino Code
In Arduino IDE write the following code.
#define ESP8266_BAUD 9600 void setup()
#include <ESP8266_Lib.h> {
#include <BlynkSimpleShieldEsp8266.h> Serial.begin(9600);
#include <SoftwareSerial.h> EspSerial.begin(ESP8266_BAUD);
char auth[] = "YourAuthToken"; delay(10);
char ssid[] = "YourNetworkName"; Blynk.begin(auth, wifi, ssid, pass);
char pass[] = "YourPassword"; }
SoftwareSerial EspSerial(2, 3); void loop()
ESP8266 wifi(&EspSerial);

## Slide 10: Install APM Planner or Mission Planner
ArduPilot is the Flight Control Board.
APM Planner is a software for configuring the drone.
Download the APM Planner from http://firmware.ardupilot.org/
Use AMP Planner or Mission Planner with version 2.0
After installation, open the APM Planner or Mission Planner Interface.

## Slide 11: APM Planner version 2.0

## Slide 12: APM Planner version 2.0
Quick Actions Status Messages
GPS Fix() GPS HDOP()
GPS Sats (n) Alt MSL (m)
Alt REL (m) Battery (%)
Climp (m/s) Current (A)
Pitch (deg) Roll (deg)
Voltage (V) Yaw (deg)

## Slide 13: APM Planner version 2.0
At the top left of APM Planner
Flight data
Flight Plan
Initial Setup
Config / Tuning : Select a baud rate of 115, 200 for a higher speed and Click on “Connect”.

## Slide 14: APM Planner version 2.0
Info View Panel – Provide the message as:
“you are about to install “ArduPilot.hex” for apm2-quad”
Click OK button to start the process.
Now the download has begun.
To see the output, check the “Show Output Option”.
After downloading, the firmware will be flashed into the ArduPilot automatically.

## Slide 15: APM Planner version 2.0
Installing ArduCopter
The version may vary depending on the version of the ArduPilot control board.

## Slide 16: Calibration
Access Calibration:
Hit the calibrate button and set in which orientation should place the drone.
Make sure the chosen orientation (above-left-right-down-up-back)
correctly.
b. Radio Calibration:
Connect the Radio transmitter with ArduPilot and click on Radio
Calibration.

## Slide 17: Radio Calliberation

## Slide 18: Calibration
c. Flight mode Calibration:
Choose any type.

## Slide 19: Calibration
Make sure all the propellers are moving.
Now we can throttle the motors gradually.
When (thrust > drone weight), the drone will start hovering.
Bring the drone 2 meters away, then move the Pitch and Roll of transmitter and control the drone.

## Slide 20: Callibration
To stop the drone from flying
- Remove the finger from the roll / pitch gimbal and slowly decrease
the throttle.
- Gradually land the drone in ground.
- When the drone almost on the ground, just push the throttle gimbal to
the button left and hold it until all the propellers stop.
Extra Precautions
- Switch off the transmitter.
- Remove the battery.

## Slide 21
Required Components and their Functions
Required Softwares (Current if any)
Tracing Assembly
Discussion

## Slide 22: Making a Follow Me drone using ArduPilot
Buy a USB dongle, which is a GPS receiver.
Official is – GlobalSat ND-100S USB GPS dongle.
(OR)
3. GPS-embedded Bluetooth module such as GlabalSat BT-368i
Bluetooth GPS receiver.
We need “telemetry” for setting up the modules with the ArduPilot software.
Settings:
Take your drone to a suitable place for flying and connect it via “MAVLink” using telemetry.
Connect your USB dongle or Bluetooth receiver to your laptop.

## Slide 23: Making a Follow Me drone using ArduPilot

## Slide 24: Making a Follow Me drone using ArduPilot
Once connect the USB dongle to the Mission Planner software, the drone will consider the dongle the “Fly to Here” location all the time.
Now, if we move our laptop, the drone will follow the laptop.
Whether always bring the laptop?
We can walk with Dongle is enough.
How?

## Slide 25: DroidPlanner 2
Download and install DroidPlanner 2 software.
Open the application.

## Slide 26: DroidPlanner 2
2. Connect OTG cable/converter to Phone and connect the USB telemetry,
such as SiK Telemetry Radio to the phone via OTG.

## Slide 27: DroidPlanner 2
3. From the home menu, Select “Loiter” as the flight mode.
(we can change it while flying too)

## Slide 28: DroidPlanner 2
4. Click the “Dronie” icon at the bottom of the screen, the drone is now a
“Follow Me Drone”
5. We can move with our phone then the drone follow the phone.
6. Now, we can control the drone from the application.
7. We can see all the flight data on the screen and know the drone’s
condition.
Note: Enable the location of the phone before using the DroidPlanner.

## Slide 29: Discussion
Required Components and their Functions
Control Settings

## Slide 30
Thank You
&
Queries?