## Slide 1: Error Detection and Correction
Types of Errors
Detection
Correction

## Slide 2
Basic concepts
Networks must be able to transfer data from one device to another with complete accuracy.
Data can be corrupted during transmission.
For reliable communication, errors must be detected and corrected.
Error detection and correction are implemented either at the data link layer or the transport layer of the OSI model.

## Slide 3
Types of Errors

## Slide 4
Single-bit error

## Slide 5
Single bit errors are the least likely type of errors in serial data transmission because the noise must have a very short duration which is very rare. However this kind of errors can happen in parallel transmission.

## Slide 6
Burst error

## Slide 8
The term burst error means that two or more bits in the data unit have changed from 1 to 0 or from 0 to 1.
Burst errors does not necessarily mean that the errors occur in consecutive bits, the length of the burst is measured from the first corrupted bit to the last corrupted bit. Some bits in between may not have been corrupted.

## Slide 9
Burst error is most likely to happen in serial transmission since the duration of noise is normally longer than the duration of a bit.
The number of bits affected depends on the data rate and duration of noise.

## Slide 10: Error detection
Error detection means to decide whether the received data is correct or not without having a copy of the original message.
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination.
Notes: Make sense of message.
Make sense of message.

## Slide 11
Redundancy

## Slide 12
Four types of redundancy checks are used
in data communications

## Slide 13
Vertical Redundancy Check
VRC

## Slide 14: Performance
It can detect single bit error
It can detect burst errors only if the total number of errors is odd.

## Slide 15
Longitudinal Redundancy Check
LRC

## Slide 16
Performance
LCR increases the likelihood of detecting burst errors.
If two bits in one data units are damaged and two bits in exactly the same positions in another data unit are also damaged, the LRC checker will not detect an error.

## Slide 17
VRC and LRC

## Slide 18: CYCLICCODES
Cyclic codes are special linear block codes with one extra property. In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword.
10101000 (Send)  01010001(one left shift)

## Slide 19: A CRC code with C(7, 4)

## Slide 20: CRC encoder and decoder

## Slide 21: Division in CRC encoder

## Slide 22: Division in the CRC decoder for two cases

## Slide 23
Polynomial

## Slide 24
Polynomial and Divisor

## Slide 25
Standard Polynomials

## Slide 26
Checksum

## Slide 27: At the sender
The unit is divided into k sections, each of n bits.
All sections are added together using one’s complement to get the sum.
The sum is complemented and becomes the checksum.
The checksum is sent with the data

## Slide 28: At the receiver
The unit is divided into k sections, each of n bits.
All sections are added together using one’s complement to get the sum.
The sum is complemented.
If the result is zero, the data are accepted: otherwise, they are rejected.

## Slide 29: Performance
The checksum detects all errors involving an odd number of bits.
It detects most errors involving an even number of bits.
If one or more bits of a segment are damaged and the corresponding bit or bits of opposite value in a second segment are also damaged, the sums of those columns will not change and the receiver will not detect a problem.

## Slide 30: Error Correction
It can be handled in two ways:
receiver can have the sender retransmit the entire data unit.
The receiver can use an error-correcting code, which automatically corrects certain errors.

## Slide 31: Single-bit error correction
To correct an error, the receiver reverses the value of the altered bit. To do so, it must know which bit is in error.
Number of redundancy bits needed
Let data bits = m
Redundancy bits = r
Total message sent = m+r
The value of r must satisfy the following relation:
2r ≥ m+r+1

## Slide 32
Error Correction

## Slide 33
Hamming Code

## Slide 34
Hamming Code

## Slide 35
Hamming Code

## Slide 36
Example of Hamming Code

## Slide 37
Single-bit error

## Slide 38
Error
Detection