## Slide 1
Network Layer:
Routing

## Slide 2: 22-1 DELIVERY
The network layer supervises the handling of the packets by the underlying physical networks. We define this handling as the delivery of a packet..
22.2
Topics discussed in this section:
Direct Versus Indirect Delivery

## Slide 3: Figure 22.1 Direct and indirect delivery
22.3

## Slide 4: 22-2 FORWARDING
Forwarding means to place the packet in its route to its destination. Forwarding requires a host or a router to have a routing table.. When a host has a packet to send or when a router has received a packet to be forwarded, it looks at this table to find the route to the final destination.
Topics discussed in this section: Forwarding Techniques Forwarding Process
Routing Table
22.4

## Slide 5: Figure 22.2 Route method versus next-hop method
22.5

## Slide 6: Figure 22.3 Host-specific versus network-specific method
22.6

## Slide 7: Figure 22.4 Default method
22.7

## Slide 8: Figure 22.5 Simplified forwarding module in classless address
22.8

## Slide 9: Note
In classless addressing, we need at least four columns in a routing table.
22.9

## Slide 10: Example 22.1
Make a routing table for router R1, using the configuration in Figure 22.6.
Solution
Table 22.1 shows the corresponding table.

## Slide 11: Figure 22.6 Configuration for Example 22.1

## Slide 12: Table 22.1 Routing table for router R1 in Figure 22.6

## Slide 13: Example 22.2
Show the forwarding process if a packet arrives at R1 in Figure 22.6 with the destination address 180.70.65.140.
Solution
The router performs the following steps:
The first mask (/26) is applied to the destination address. The result is 180.70.65.128, which does not match the corresponding network address.
The second mask (/25) is applied to the destination address. The result is 180.70.65.128, which matches the corresponding network address. The next-hop address and the interface number m0 are passed to ARP for further processing.

## Slide 14: Example 22.3
Show the forwarding process if a packet arrives at R1 in Figure 22.6 with the destination address 201.4.22.35.
Solution
The router performs the following steps:
1. The first mask (/26) is applied to the destination address. The result is 201 4 22 0, which does not match the corresponding network address.
2 The second mask (/25) is applied to the destination address. The result is 201.4.22.0, which does not match the corresponding network address (row 2).

## Slide 15: Example 22.3 (continued)
3. The third mask (/24) is applied to the destination address. The result is 201.4.22.0, which matches the corresponding network address. The destination address of the packet and the interface number m3 are passed to ARP.

## Slide 16: Example 22.4
Show the forwarding process if a packet arrives at R1 in Figure 22.6 with the destination address 18.24.32.78.
Solution
This time all masks are applied, one by one, to the destination address, but no matching network address is found. When it reaches the end of the table, the module gives the next-hop address 180.70.65.200 and interface number m2 to ARP. This is probably an outgoing package that needs to be sent, via the default router, to someplace else in the Internet.

## Slide 17: Figure 22.7 Address aggregation

## Slide 18: Figure 22.8 Longest mask matching

## Slide 19: Example 22.5
As an example of hierarchical routing, let us consider Figure 22.9. A regional ISP is granted 16,384 addresses starting from 120.14.64.0. The regional ISP has decided to divide this block into four subblocks, each with 4096 addresses. Three of these subblocks are assigned to three local ISPs; the second subblock is reserved for future use. Note that the mask for each block is /20 because the original block with mask /18 is divided into 4 blocks.
The first local ISP has divided its assigned subblock into 8 smaller blocks and assigned each to a small ISP. Each small ISP provides services to 128 households, each using four addresses.

## Slide 20: Example 22.5 (continued)
The second local ISP has divided its block into 4 blocks
and has assigned the addresses to four large
organizations.
The third local ISP has divided its block into 16 blocks
and assigned each block to a small organization. Each small organization has 256 addresses, and the mask is
/24.
There is a sense of hierarchy in this configuration. All routers in the Internet send a packet with destination address 120.14.64.0 to 120.14.127.255 to the regional ISP.

## Slide 21: Figure 22.9 Hierarchical routing with ISPs

## Slide 22: Figure 22.10 Common fields in a routing table

## Slide 23: Example 22.6
One utility that can be used to find the contents of a routing table for a host or router is netstat in UNIX or LINUX. The next slide shows the list of the contents of a default server. We have used two options, r and n. The option r indicates that we are interested in the routing table, and the option n indicates that we are looking for numeric addresses. Note that this is a routing table for a host, not a router. Although we discussed the routing table for a router throughout the chapter, a host also needs a routing table.

## Slide 24: Example 22.6 (continued)
The destination column here defines the network address. The term gateway used by UNIX is synonymous with router. This column actually defines the address of the next hop. The value 0.0.0.0 shows that the delivery is direct. The last entry has a flag of G, which means that the destination can be reached through a router (default router). The Iface defines the interface.

## Slide 25
Example 22.6 (continued)
More information about the IP address and physical address of the server can be found by using the ifconfig command on the given interface (eth0).

## Slide 26: Figure 22.11 Configuration of the server for Example 22.6

## Slide 27: 22-3 UNICAST ROUTING PROTOCOLS
A routing table can be either static or dynamic. A static table is one with manual entries.. A dynamic table is one that is updated automatically when there is a change somewhere in the Internet.. A routing protocol is a combination of rules and procedures that lets routers in the Internet inform each other of changes..
Topics discussed in this section:
Optimization
Intra- and Interdomain Routing Distance Vector Routing and RIP Link State Routing and OSPF Path Vector Routing and BGP

## Slide 28: Figure 22.12 Autonomous systems

## Slide 29: Figure 22.13 Popular routing protocols

## Slide 30: Figure 22.14 Distance vector routing tables

## Slide 31: Figure 22.15 Initialization of tables in distance vector routing

## Slide 32: Note
In distance vector routing, each node shares its routing table with its immediate neighbors periodically and when there is a change.

## Slide 33: Figure 22.16 Updating in distance vector routing

## Slide 34: Figure 22.17 Two-node instability

## Slide 35: Figure 22.18 Three-node instability

## Slide 36: Figure 22.19 Example of a domain using RIP

## Slide 37: Figure 22.20 Concept of link state routing

## Slide 38: Figure 22.21 Link state knowledge

## Slide 39: Figure 22.22 Dijkstra algorithm

## Slide 40: Figure 22.23 Example of formation of shortest path tree

## Slide 41: Table 22.2 Routing table for node A

## Slide 42: Figure 22.24 Areas in an autonomous system

## Slide 43: Figure 22.25 Types of links

## Slide 44: Figure 22.26 Point-to-point link

## Slide 45: Figure 22.27 Transient link

## Slide 46: Figure 22.28 Stub link

## Slide 47: Figure 22.29 Example of an AS and its graphical representation in OSPF

## Slide 48: Figure 22.30 Initial routing tables in path vector routing

## Slide 49: Figure 22.31 Stabilized tables for three autonomous systems

## Slide 50: Figure 22.32 Internal and external BGP sessions